## Slide 1: Real-Time Illegally Parked Vehicle Detection (RTIPVD)
Final Evaluation
Team members :
Himanshu Harshit Singh K. Shubham Harshit Kshitiz Singh
,

## Slide 2: Problem and our contribution
The Problem
Our Solution
Existing systems rely on fixed CCTV — no mobile coverage
No ego-motion compensation → false detections from moving cameras
Hard-coded thresholds fail across different environments
No evidence capture — no plate, no GPS, no challan
Works on dashcam, drone & patrol vehicle — no fixed infra needed
Lane-anchored ego-motion compensation using RANSAC homography
Auto-calibrating adaptive threshold (P80, first 60 frames)
Full evidence: OCR plate + GPS coordinates + timestamp + photo

## Slide 3: System Architecture
HARDWARE LAYER
📷 Camera
Dashcam mounted on patrol vehicle
🍓 Raspberry Pi 4
Edge orchestrator — capture + stream
📡 GPS Module
Real-time coordinate logging
🌐 Wi-Fi / LTE
Live video stream to server
SERVER / SOFTWARE LAYER
1
YOLOv8 + ByteTrack
Vehicle detection & multi-object tracking
2
Ego-Motion Compensation
LK optical flow + RANSAC homography on lane markings
3
Parking State Engine
Adaptive P80 threshold + EMA smoothing + forgiveness frames
4
Smart OCR Pipeline
CLAHE → EasyOCR → regex → majority voting
5
GPS Evidence Logger
Coordinates + plate + timestamp + cropped image → SQLite DB + REST API dashboard

## Slide 4: Novelty – What Sets RTIPVD Apart
1
Moving Camera Compatible
Works from dashcams, drones, patrol vehicles — unlike all fixed CCTV systems
2
Lane-Anchored Ego-Motion Compensation
Lane optical flow = exact camera motion; vehicle motion minus lane = true absolute motion
3
Homography-Based Perspective Transform
RANSAC homography handles rotation, zoom & perspective — not just simple translation
4
Auto-Calibrating Adaptive Threshold
P80 percentile over first 60 frames; auto-adapts to resolution, speed, lighting
5
Jitter-Resilient Classification
EMA centroid smoothing + forgiveness frames prevent false resets from YOLO box jitter
6
GPS-Anchored Target Geolocation
Patrol GPS + camera geometry → exact coordinates of the violator vehicle, not observer
Smart OCR Pipeline
7
OCR activates ONLY for stopped vehicles; CLAHE → EasyOCR → regex → majority voting

## Slide 5: Results and deliverables
YOLOv8
Custom Trained
Parking vehicle detection
ByteTrack
Multi-Object
Vehicle tracking across frames
EasyOCR
Indian Plates
Regex-validated plate reading
Raspberry Pi
Edge Node
Live GPS + stream pipeline
✅ Completed Features
✓ Custom YOLOv8 vehicle detection model
✓ ByteTrack multi-vehicle tracking
✓ Lane-based ego-motion compensation (LK + Homography)
✓ Real-time parking detection from moving camera
✓ EasyOCR plate reading with regex + majority voting
✓ Adaptive threshold auto-calibration (P80)
✓ Raspberry Pi + GPS + camera hardware integration
✓ Live video streaming to remote server
✓ GPS-tagged violation evidence + SQLite storage
Evidence Package on Violation
📸 Cropped vehicle photo
🔤 OCR'd license plate number
📍 GPS coordinates of violation
🕐 Timestamp of detection
📊 Confidence score

## Slide 6: Team contribution and Conclusion
Himanshu
Project Lead & CV Core
• YOLOv8 model training & fine-tuning
• Ego-motion compensation (LK optical flow + RANSAC)
• Adaptive threshold calibration
• Overall system integration
Harshit
Tracking & State Engine
• ByteTrack multi-vehicle tracker integration
• Jitter-resilient EMA centroid smoothing
• Forgiveness frame logic for parking state
• Real-time performance optimization
Harshit Singh
OCR & Evidence Pipeline
• CLAHE image enhancement for plates
• EasyOCR + Indian regex validation
• Temporal majority voting for plate accuracy
• Evidence package generation
K. Shubham
Hardware & GPS Integration
• Raspberry Pi + camera + GPS setup
• GPS coordinate timestamping & logging
• Live video streaming to server
• GPS-to-violation coordinate mapping
Kshitiz Singh
Backend & Infrastructure
• Server-side video processing pipeline
• Database design for violation records
• System architecture & API design
• Testing, QA & documentation
"From a computer vision prototype to a fully deployed GPS-integrated mobile enforcement system — built end-to-end at IIT Roorkee."

## Slide 7
Thank you !!